## Slide 1: Can You Even Debug a 200M+ Gate Design?
Horace Chan
PMC-Sierra
Brian Vandegriend
PMC-Sierra
Deepali Joshi
PMC-Sierra
Corey Goss
Cadence

## Slide 2: Overview:
Debug techniques for a 200M+ gate design
Testbench built in Specman UVMe
  Simulator: Cadence IES
Speed up debug turnaround time for RTL
  saving and Loading Checkpoint Snapshots
  dynamic Load Additional Code at Saved Checkpoints
  waveform Verbosity
Speed up debug turnaround time for testbench/software
  incremental compile of the Specman testbench
  software/Hardware co-verification

## Slide 3: Saving and Loading Checkpoint Snapshots
Problem:
  Long simulation time
  Need to wait a long time to reproduce the failure
  Probing waveform slow down the simulation even more
Solution:
  Save a checkpoint snapshot every 30 minutes
  Save a checkpoint snapshot every 1ms of run time
  Save a checkpoint after each key testflow phase
  Rerun from the save checkpoint to reproduce the failure

## Slide 4: Saving and Loading Checkpoint Snapshots (Implementation)
Checkpoint period controlled by
  Environment variables
  Shell script arguments
  vManager VSIF attributes
  e constrains
Optimal checkpoint period depends on the snapshot size and the load of the network
  E.g. 30 seconds checkpoint saving overhead for a 4G snapshot during work hours

## Slide 5: Dynamic Load Additional Code at Saved Checkpoints
Unique feature of Specman and the e language
Can load additional e code after loading a snapshot to:
  Change the constraint of a sequence
  Modify the behavior of existing methods
  Add and launch new sequence
The testbench is built with empty method hooks between each key testflow phase for dynamic load extension

## Slide 6: Dynamic Load Additional Code at Saved Checkpoints (use case)
Add extra debug code to print more information
  Change the sequence stimulus generation around the failure point to explore the bug
Test different what-if scenarios without waiting for the simulation to run from time zero
  Skip the 3 hours wait to configure the device and wait for the traffic to stabilize
Group regression runs that share a common initial period to reduce CPU and license usage

## Slide 7: Waveform Verbosity
Same idea as message verbosity
  The less waveform probed, the faster the simulation
  The more waveform probed, the more debug info
Easy control to set the waveform verbosity at run time
Suggested verbosity level
  NONE: No waveform is probed
  LOW: Probe all the ports of the module
  MEDIUM: Probe all the internal signals of the module
  HIGH: Probe the memories and variables of the module
  FULL: Probe delta cycle changes of the signals

## Slide 8: Checkpoint Usage Example

## Slide 9: Incremental compile of the e testbench
Compiled testbench runs 3x faster
Interpreted testbench has better debug support
  Can reload the testbench without exiting the simulator
    Keep the CPU and license
  Can keep the current state of the simulation without rewinding back time zero
    Loading initial snapshot takes a long time
The best of both worlds:
  Can compile stable testbench code for optimal performance
  Code still under development can be run in interpreted mode for optimal debug

## Slide 10: Software/Hardware co-verification
Integrate software (C code) with the testbench (e code)
  The C code is running on the Linux host as a thread inside the simulator
    1000x faster than running inside the CPU RTL
    100x faster than running with CPU model
  Replay the software calls without the simulator
    Reduce software debug turnaround time from 30 minutes to 30 seconds
  SimVision GUI has source debugger for all languages in the testbench and DUT. (e, C, Verilog/VHDL/SV)
Implementation details refer to:
  Hardware/Software Co-Verification Using Specman and SystemC with TLM Ports, DVCON2011

## Slide 11: Benefits and results
Speed up the RTL debug turnaround time by 90%
  Average time to failure in simulation is 6 hours
  Reduce overall development time by 50%
The compiled testbench is running 300% faster
  Specman CPU usage: 15% down to 5%
Silicon bring up in the lab with already tested software
  From 2-3 weeks down to 1-2 days

## Slide 12: Future development
Port to SystemVerilog and other simulators
  Saving and Loading Checkpoint Snapshots
    Easy to port. If the simulator supports saving checkpoint.
  Dynamic Load Additional Code at Saved Checkpoints
    Impossible to port. Unique feature in Specman
  Waveform Verbosity
    Easy to port. The code is implemented in tcl
  Incremental compile of the Specman testbench
    Hard to port. Unless SV supports AOP
  Software/Hardware co-verification
    Easy to port. SV supports DPI-C programming interface too.