## Slide 1: Maximize Vertical Reuse, Building Module to System Verification Environments with UVMe
Horace Chan
PMC-Sierra
Brian Vandegriend
PMC-Sierra
Deepali Joshi
PMC-Sierra
Corey Goss
Cadence

## Slide 2: What is vertical reuse?
Horizontal Reuse
  Reuse VIP across different projects
Vertical Reuse
  Reuse new VIP, sequences, checkers among module, subsystem and system testbenches in the same project
Maximize Vertical Reuse
  Import full module testbenches to subsystem testbench
  Import full subsystem testbeches to system testbench
  Stitch subsystem testcases to create system testcase

## Slide 3: Benefits of vertical reuse
Parallel development of all testbenches
Plug-n-play architecture to integrate system level testbench from module and subsystem testbenches seamlessly
Increase verification efficiency
  No duplication of development effort
  Less testbench code maintenance
    Changes in lower level testbench is propagated up automatically
  Better debug support from lower level testbench
    All lower level testbench the checkers and monitors are available
  Easier to move verification engineers among module, subsystems and system level testing

## Slide 4: The testbench architecture
200+ Million Gates Design
  Partition into 10 subsystems and over 50 modules
  Over 20 subsystem and module testbenches
Testbench implemented in Specman UVMe
  All VIPs communicate using TLM interface
The system testbench is integrated in 1 month
  2-3 days to bring in a new subsystem testbench
  Early initial system level testing while subsystem testbench is still finalizing features

## Slide 5: System UVC Architecture
Based on Cadence’s System UVC Architecture
Module UVC
  No master virtual sequence or register sequence
  UVCs are layered using TLM ports
  Separate protocol UVCs from interface UVCs that drive the RTL signals
System UVC is created by putting together multiple module UVCs

## Slide 6: System UVC Example

## Slide 7: TLM port router
TLM port limitations:
TLM transport port does not support one-to-many binding
TLM analysis port always broadcast
Port binding is static in the simulation
Solution: TLM port router to support dynamic many-to-many port binding with build-in routing table
// sample implementation of TLM analysis port router
template unit port_router_u of (<type>) {
in_ports : list of in interface_port of tlm_analysis
of <type> is instance;
out_ports : list of out interface_port of tlm_analysis
of <type> is instance;
get_channel_id(tr : <type>) : uint is {};
set_channel_id(tr : <type>, cid : uint) is {}
routing_table : list of src_route_table_entry_s;
};
struct dest_route_table_entry_s {
enable : bool;
port_id : uint;
channel_id : uint;
};
struct src_route_table_entry_s {
enable : bool;
port_id : uint;
channel_id : uint;
destinations : list of dest_route_table_entry_s;
};

## Slide 8: Common UVC Configuration Control
Unify data structure to control TLM port binding in module UVC
Enable/disable each individual UVC, checker, scoreboard inside the module UVC
Preserve all the binding information of the module UVC in system UVC
// sample common config control data structure definition
struct config_ctrl_s {
layer_name : layer_t;
enable : bool;
is_active : uvm_active_passive_t;
bind_enable : bool;
};
struct port_config_ctrl_s {
port_name : port_t;
layer_config : list of config_ctrl_s;
};
extend uvm_env {
config_ctrl_table : list of port_config_ctrl_s;
get_uvc_enable(port:port_t, layer:layer_t) : bool is {};
get_uvc_is_active(port:port_t, layer:layer_t)
: uvm_active_passive_t is {};
get_uvc_bind_enable(port:port_t, layer:layer_t)
: uvm_active_passive_t is {};
};

## Slide 9: Common Test Flow Virtual Sequence
Testflow to co-ordinate and synchronize the behavior of imported module UVCs virtual sequences
Testflow phases are implemented as empty TCM methods in the virtual sequence base class
Module UVC fill in testflow phases using extension

## Slide 10: Benefits and results
Statistic Measure | Previous Project | Current Project | Changes
Gates count | 60M | 200M | +133%
Total lines of code | 575k | 484k | -16%
System testbench line of code | 324k | 215k | -34%
% system testbench in total code | 56% | 44% | -22%
Gates verified per line of code | 104k | 413k | +400%
Less code, less bugs
More reuse, higher quality of the code
System level testcase as short as 20 lines of code
Better system level debug support from subsystem and module level verification engineers

## Slide 11: Challenges and Solutions
Revision conflict of common VIP used by the testbenches
  Solution:
    Freeze common VIP revision early
    Make sure new revision is backward compatible
    Co-ordinate upgrade of non-backward compatible VIP revision across all testbenches
Poor quality code imported from lower level testbench impact simulation performance
  Solution:
    All testbenches should run profiling to identify CPU and memory bottleneck
    Frequent code review by experienced engineers

## Slide 12: Future development
Port the framework to SystemVerilog UVM
SV does not support Aspect Oriented Programming (AOP)
  Possible to work around using design patterns
    More lines of code and complex TB structure
    More upfront planning for hooks and APIs
    More intrusive code maintenance
    More revision control discipline
e constructs used in the framework
  e template -> SV parameterized type
  e keyed list -> SV associate array
  e predefined routines -> SV macro-based util libraries