## Slide 1: A Methodology to Port a Complex Multi-Language Design and Testbench for Simulation Acceleration
Horace Chan, PMC
Brian Vandegriend, PMC
Efrat Shneydor, Cadence

## Slide 2: Why Simulation Acceleration
1 2 10 100 108 1010
Hard
Easy
Extra Effort
Speed Up
RTL
Simulation
ICE
Embedded Testbench
TBA Acceleration
Signal
Acceleration

## Slide 3: Benchmark Results
 | Project A (2012) | Project B (2014) | Project C (2014)
Design size (in Mgates) | 26 | 38 | 50
Domains used | 6 | 6 | 8
Speedup factor | 40x | 67x | 52x
Migration Schedule | > 1 year | 3 months | 3 weeks

## Slide 4: 4 Types of Simulations
Type | Where the RTL runs | Objectives
Normal | RTL Simulator | TB profiling, optimization Generate golden reference
SA_SIM | RTL Simulator | Debug SCEMI-pipe Debug DPI integration Clean up TB-RTL binding
SA_SW | SW model of the Box | Debug RTL synthesis flow Setup shell scripts for SA
SA_HW | The Box | Debug mismatch between SW model and the Box Benchmark SA

## Slide 5: Compile the RTL
If the RTL won’t compile, there is zero speedup
Every VHDL/Verilog/SV compiler is not the same
Use the same tool chain from the same vendor
Don’t hack the RTL to work around tool problems
  fix the tool!
Use the same workspace as normal simulation
Reuse compile scripts from ICE flow
  Use SV config to swap in TBA components

## Slide 6: Testbench Enhancement
Testbench is the bottleneck
  Transaction based processing is a must
  TB should use less than 2-3% CPU cycle
Clean interface between TB and RTL
  No wait delay
  No direct RTL signal access
  No cycle by cycle interaction

## Slide 7: Testbench Enhancement
Specman makes the TB upgrade easy
Use AOP to keep TB code for normal simulation and acceleration in two different aspects
  No messy factories or callback functions
Use powerful macros and reflection interface to catch unknown TB-RTL interaction
  Build debug tools to inspect the TB code

## Slide 8: TB/box communication
Mechanism | When to use
SCE-MI pipe | Transfer larger chuck of data TLM port on TB side FIFO on RTL side
e/SV DPI Interface | Light weight control protocols Timing sensitive trigger functions
MARG (direct memory copy) | One-off deposit or read Custom pipe implementation Backdoor access
Tcl force, deposit, value | The last resort solution No recompile is required

## Slide 9: Regression Management
Use the same regression tool as normal simulation
  SA is like a super fast computer
Download snapshot to the box is slow
  Download once, run all the sims in the same session
Auto re-launch overnight failed sims
  SA_HW is too expensive for interactive debug
  Hot swap to SA_SW before the failure point
No checkpoint save and restore in SA (yet)

## Slide 10: Conclusion
Focus on quick bring up of SA
Don’t optimize for the best possible speed up
  SA can never run as fast as ICE
Positive ROI around 30-40x speed up*
  In terms of raw simulation through put
  * depends on the license fees discount and acceleration box lease contract
Faster debug turnaround time = higher productivity

## Slide 11
Q & A