## Slide 1: How to test the whole firmware/software when the RTL can’t fit the emulator
Horace Chan, Byron Watt – Microchip Technology
Optional Company Logo
(show on Title Slide ONLY

## Slide 2: Agenda
Introduction
Challenges
Existing Solutions
Architecture of the Hybrid Software Simulator
Use Mode on Testing User Space FW
Use Mode on Testing Kernel Space FW
Results

## Slide 3: Introduction
Pre-silicon FW/SW testing using emulation is a MUST
  Catch system bugs before tape-out

## Slide 4: The problem
The design is too big to fit in the emulator
  Buy bigger emulators (if you ask the EDA vendor)
  $$$$
Borrow an idea from verification
  Blackboxes RTL logic not required by the test
  Build multiple design snapshots for different test scenarios
  Save up to 50% of gates on average

## Slide 5: Challenges
Notes: Access blackboxed addresses
AXI bus lock up
CPU stalls
PCIe hangs
host Linux freezes

## Slide 6: Existing Solutions
Run block level FW in verification TB
  Tried this approach in previous project
  Can’t test the whole FW/SW before silicon
  Can’t find integration bugs
  The verification team hate it.
    Extra C code to debug on top of the RTL.
    The FW is not as verification-friendly as UVM sequences

## Slide 7: Existing Solutions
Use of #ifdef or makefile parameters to partition the FW
  Tried this approach in previous project
  Spent lots of unproductive hours hacking the FW code
    add #ifdef all over the place
    create mock function to bypass register access into blackboxed addresses
  It is a maintenance nightmare on RevB
  This solution doesn’t scale

## Slide 8: Existing Solutions
Insert dummy AXI/AHB slave components in the blackboxed RTL
  Investigated this approach in the beginning of this project
  Too much work to create the blackboxed SV modules
  Too much work to hack the RTL compile script for emulation
  Can’t model the blackboxed RTL behavior
    AXI/AHB dummy only returns zero on read

## Slide 9: Existing Solutions
Use of a Virtual Platform
  Investigated this approach in the beginning of this project
  Too time consuming to setup QEMU proxy and SystemC models
  Inconvenient to debug the FW code compare to our approach
  Doesn’t work for us, but it might be the right choice for a different project

## Slide 10: Our Hybrid Emulation Scenario
A x86 Linux server controls multiple chips via PCIe bus in the production environment
The PCIe bus is replaced by the PCIe speed bridge in the emulation environment
The embedded CPU inside the chip is also running Linux
The SW running on the host Linux communicates with the FW running inside the embedded Linux via TCP sockets or PCIe mailbox.
The end-user has no direct access into the FW. The end-user interacts with the FW through the public API of the SW running on the host Linux

## Slide 11: Hybrid SoftWare SIMulator
Notes: Generate from register description files (IP-XACT)
  Hybrid Software Simulator
  System Verilog register implementation
  C header files for the FW
    embedded view (direct AXI write/read)
    HSWSIM view (TCP to HSWSIM)
Features of the Hybrid Software Simulator
  Shadow register bank
  Address filter/translator to the emulator
  Trigger callback functions to model RTL behavior

## Slide 12: Test User Space FW
Notes: User Space FW are non-timing critical
  Extra latency of PCIe is irreverent
Run everything on host Linux
  Faster debug turn around time
  Can use any IDE as the gdb client
Can mix and match TB config sequences with the FW

## Slide 13: Test Kernel Space FW
Notes: Kernel space FW are ISR and Linux drivers
  Has to run on the embedded CPU
User space FW is already bug free
Fake the behavior of blackboxed RTL with HSWSIM
Debug like real silicon
  printk on UART,
  DSTREAM on JTAG
Note: RTL used by the kernel space code cannot be blackboxed

## Slide 14: Results (pre tape-out)
All major FW features are tested in emulator
  Design running at 5Mhz in the emulator
  Linux boots up in less than 5 minutes
  Found 3 RTL bugs before tape-out

## Slide 15: Results (Silicon)
Smoothest bring up for a Rev A device
  Linux and FW running on day 1
  First major feature running on day 3 (debug non-digital FW code)
  All major features running on the first week
  First FW release to customers in less than a month
  Pin point a corner case RTL bug discovered in Silicon testing
    Simulation can’t reproduce the bug, it takes a few seconds to run on silicon
    Emulation sees the bug, dump waveform and let the designer diagnose the problem.
    With the new insight from emulation, simulation is able to reproduce the bug in 2 hours

## Slide 16
Q & A