## Slide 1: Speedup the Debug Turnaround Time and Regression Run Time with SystemVerilog/UVM Test Dynamic Load
Horace Chan

## Slide 2: Agenda
Overview
What’s New in Xcelium
Syntax and Tips
Use Model
Benefits and Results
Roadmap

## Slide 3: Company Overview

## Slide 4: Optical Networking

## Slide 5: Specman vs System Verilog
SystemVerilog is SLOW to debug
  Primitive peek/poke/force only
  No user inputs
  Can’t change TB behavior once the simulation is running
  Recompile, recompile, recompile
Specman is FAST to debug
  Call any testbench function in run time
  No recompile is needed
  Support dynamic load of additional code at saved checkpoints
    Rewrite existing sequence
    Modify the behavior of existing methods
    Add and launch new sequence

## Slide 6: What’s in Xcelium
SystemVerilog/UVM Dynamic Test Load
  Load new SV package into saved snapshot
  Call testbench functions when the snapshot is reloaded
Dynamic Base Snapshot (DBS)
  Time zero snapshot or saved snapshot
Dynamic Test Snapshot (DTS)
  Contains the incremental new SV package

## Slide 7: Syntax
Elaborate the Dynamic Base Snapshot
xrun –f base_ve_stuff.f \
  -f dut_stuff.f \
  -uvm \
  -mkdbssnap –checkpoint_enable –plusarg_save\
  -name dbsnap
Elaborate the Dynamic Base Snapshot
xrun new_test_pkg.sv \
  -uvm –uvmnoautocompile \
  -dbssnap after_initialization \
  -dbsname dbsnap \
  -name dbsnap
  -input new_test.tcl

## Slide 8: Save a snapshot
Use $save() SV system task in the TB
$save(“after_initialization”)
Use ncsim tcl save command in run time
xrun> save after_initialization
Does not support save into a different path in run time
  Use –cds_implicit_tmpdir as a workaround at start time
Supports save into a different library
Watch out for cds library size explosion
Watch out for cds library lock

## Slide 9: Override existing sequence after reload
Use tcl UVM command
uvm_factory –override –by_type \
old_test_seq new_test_seq
run
Use SV plus options in TB
uvm_cmdline_processor clp = new;
clp.get_arg_value(“+TEST_SEQ=“, test_seq);
w = factory.find_by_name(test_seq);
$cast(seq, factor.create_object_by_type(w,…);
Watch out: don’t use default UVM cmdline processor
  Its SV plus options is not updated after reload
  Always create your own new instance after reload

## Slide 10: Call testbench function/task after reload
package new_pkg;
class new_code:
function new():
fork
uvm_root uvm_top = uvm_root::get();
tb_ve ve = uvm_top.find(“uvm_top.ve”);
// call testbench functions or tasks
ve.foo();
ve.bar();
join_none;
endfunction
endclass
new_code mycode = new;
endpackage

## Slide 11: Exit after saving a snapshot
Use tcl variable to store exit state
  Clear the tcl variable after reload
Use SV-DPI to call tcl prompt from SV (see cdnshelp)
task save_cp(string cp_name, bit exit);
if (exit == 1) begin
dpi_tcl_exec_cmd(“set exit_after_cp 1”);
end
$save(string_t’(cp_name));
#0;
tcl_rv = 0;
dpi_tcl_exec_cmd(“deposit tcl_rv [info exists exit_after_cp]”);
if (tcl_rv == 1) begin
$finish;
end
endtask

## Slide 12: Use Model
Compile DUT and stable part of the TB with MSIE
  Save a Dynamic Base Snapshot at time zero
  Put each testcase and sequences in flux into its own package
MSIE elab time 5 mins vs DTS elab time 30 seconds
Probe minimum waveform to speed up simulation
Save a checkpoint periodically
Save a checkpoint after each key test phase
  Rerun from the saved checkpoint to dump waveform for debug
  Rerun from the saved checkpoint to try different scenarios

## Slide 13: Checkpoint Usage Example

## Slide 14: Benefits and Results*
Speed up the RTL debug turnaround time by 90%
  Average time to failure in simulation is 6 hours
  Reduce overall development time by 50%
Reduce the regression time by 25%
  DUT initialization takes roughly 25%
  * Based on data from previous project using Specman SAO dynamic load
  SV dynamic load is still in alpha, not ready for deployment

## Slide 15: Roadmap
SV dynamic load still does not support:
  Simvision reinovke
  Use ncsim tcl restart command to load new SV code
  Save the checkpoint to a different path at run time
  UVM default command line processor after reload
  Xcelium mulit-core simulation
Issues with cds library corruption and lock up occasionally
  Need a tool to copy the cds library to avoid dependency between runs
Build your next testbench with SV dynamic load in mind, use it when it is ready

## Slide 16: Questions and Answers
Special thanks to
John Rose, Adam Sherer