## Slide 1: Pre-Silicon SW/FW Testing with Protium S1 – A Case Study
Horace Chan

## Slide 2: Agenda
Overview
Background
Use Model
Improvements Over Time
Roadmap
Accomplishments

## Slide 3: Company Overview

## Slide 4: Optical Networking

## Slide 5: Shift Left
Start SW testing early = sooner SW release to customers
Start SW testing early =

## Slide 6: History
run block level SW C code in verification testbench
  TB can not keep up with the changes in the SW API
  More code to test in verification
FPGA prototyping
  Require RTL modification
  Lack auto compilation (clock, partitioning, waveform)
  Slow turn around time
  Custom platform required significant development time
run full SW C code on toplevel testbench
  run time is painfully slow  limited progress

## Slide 7: Which box?
 | Palladium Z1 | Protium S1
Cost | $$$$$$$$$$$$$$$$$$$$ | $$$
Technology | Boolean processor | FPGA
Capacity | Up to 2B gates | Up to 600M gates (3 chassis)
Compile time | 2-3 hours | 2-3 days
Waveform | Just like simulator | Require recompile*
Clock Freq | 0.5 MHz | 5 MHz
Use case | RTL debug | SW debug

## Slide 8: Protium S1 setup in the lab
PCIe
JTAG
DSTREAM probe DS-5 Studio
EDK with CentOS
(equivalent to ComExpress)

## Slide 9: Testing SW with RTL
SW C code
FW C code

## Slide 10
Improvements Over Time

## Slide 11: PCIe Speed Bridge
 | Gen3 SB | Gen4 SB
Clock Freq | 0.7 MHz (1 HDDC cable) 1.4 MHz (2 HDDC cables) | 5.5 MHz
Linux boot up time | > 30 minutes | < 5 minutes (CAKE2) < 2 minutes (CAKE1)
Bring up time* | 2 weeks | 1 week
* Excluding time wasted on bad hardware (SB card, IO cards, QSS cables, PTM cables, etc)

## Slide 12: PnR time
PTM16.2
  PnR on large builds (> 50% utilization) takes 2 weeks
PTM17.1 RTM
  with hotfixes
  with undocumented PnR options from Cadence R&D
  with manual partition
  PnR on large builds takes 3 days
Tips
  Sign NDA with Cadence, so you can send all the RTL files to Cadence and let R&D debug PnR issues

## Slide 13: Dual Chassis setup
Trial run on beta box
Double the capacity
  fits more gates
Lower FPGA utilization
  much faster PnR
  50-60% on 1 box takes 1 week
    normal PnR than high PnR on failed FPGAs
  20-30% on 2 boxes takes < 2 days
    rarely requires high PnR
PTM cable configuration is not compatible with 1 chassis setup

## Slide 14: SystemVerilog Testbench over Protium
PCIe
socket
Convert AXI/APB register access into PCIe access
  Run SV config sequences as-is from the testbench
  Does not support any traffic gen/mon UVC
Drop in replacement of SW config API
  Much easier to debug SW misconfiguration than comparing register log from simulation
  SW testing is complimentary to HW verification

## Slide 15: Waveform without Recompile
In PTM16.2
  Changing the signal probes requires a new build & PNR
    Fast, 1-2 minutes to dump 8000 cycles for 200 signals in VivadoLab
In PTM17.1
  New state dump feature
    change signal probes without recompile
  Very slow, but still faster than a recompile
    dump 8000 cycles for 200 signals takes 30 minutes
    EDK/PCIe SB is dead during state dump
  Use Protium assertion as trigger
    changing the trigger still needs to recompile

## Slide 16: Road Map
Use Protium for pre-silicon software testing on future projects
  Invest in another S1 box to support dual chassis setup
  Allow us to test more SW in parallel before silicon
Investigate using Protium to speed up top-level regression in verification
  Protium is not the right tool to debug HW bugs
  but we don’t need to debug passing simulations

## Slide 17: Accomplishments
uBoot and Linux boot up
FW download
DSTEAM probe and ARM CoreSight
  SW Trace Buffer
  CPU profiling
All major datapath are up and running with SW
BONUS: Found 2 minor bugs in the RTL

## Slide 18: Questions and Answers
Special thanks to
Markus Karg, Sreenath Yaramareddy